## Slide 1
17/06/2026
Cinzia Perrino MD PhD FESC
How do I ensure environmental safety in my research lab?

## Slide 2
No conflicts to declare

## Slide 3
Why do research laboratories matter?
Yet they can account for 30–70% of total institutional energy consumption.
Laboratories occupy only a small fraction of institutional space (~5–10% in many universities and hospitals).
Typical wet laboratories consume 3–10 times more energy per square meter than office buildings.
Highly specialized facilities (animal facilities, clean rooms, biobanks) may consume 10–100 times more energy than standard offices.

## Slide 4
Direct production (onsite):
Refrigerant leaks from cooling equipment
Natural gas heating
Emergency diesel generators
Laboratory fleet vehicles
Specialty gas losses
Purchased electricity used for:
Ultra-low temperature (-80°C/-70°C) freezers
Biobank storage systems
Refrigerators and cold rooms
Incubators
Biosafety cabinets
Fume hoods
Centrifuges
Microscopes and imaging platforms
Flow cytometers
Sequencing and omics platforms
PCR and molecular biology equipment
Cell culture facilities
Laboratory lighting
HVAC (heating, ventilation, air conditioning)
Servers and local data storage
Charging laboratory equipment and devices
Purchased heating, cooling, or steam:
District heating
District cooling
Centralized steam systems
Purchased goods and services
Plastic consumables
Cell culture plastics
Reagents and chemicals
Antibodies
Kits for molecular biology
Sequencing reagents
Laboratory animals
Biological samples purchased externally
PPE (gloves, gowns, masks)
Cleaning products
Capital Goods
Freezers
Sequencers
Microscopes
Flow cytometers
Imaging systems
Computers and servers
Laboratory furniture
Scope 1
Scope 2
Scope 3
DIRECT
INDIRECT
energy/facilities
INDIRECT
supply chain or services
Scope 3
Waste
Hazardous chemical waste disposal
Biohazard waste disposal
Sharps disposal
Animal waste disposal
Recycling services
Transportation and Distribution
Business Travel
Employee Commuting
Data and Digital Infrastructure
Animal Research Activities
Feed production
Bedding materials
Supply chains supporting animal facilities
Water and Utilities
Construction and Infrastructure
Carbon Emissions from Research Laboratories
2% of global plastic waste
Biomedical laboratories can generate tens to hundreds of kilograms of plastic waste per researcher per year, with pipette tips among the largest contributors.

## Slide 5
Environmental safety in the research
laboratory: at least two sides of the moon
Safety for People
  Focuses on preventing workplace hazards including chemical exposure, biological risks, airborne contaminants, and physical safety protocols.
Safety for the Planet
  Focuses on sustainability initiatives such as reducing energy consumption, managing waste, responsible disposal, and resource conservation.
Considering human protection and planetary responsibility

## Slide 6
Chemical Safety
Laboratory risks examples
Hazardous chemical substances
  Risks include formaldehyde (carcinogen), xylene (nervous system depressant), organic solvents (flammability), and acids/bases (corrosive).
Vapors and Air
Airborne hazards
  Common sources including histology reagents, solvents, and fixatives that require controlled handling.
Biological Safety
Human and animal specimens
  Tissue samples, biopsies, cellular materials, blood and bodily fluids.
Waste
  Major waste sources
  Biological, chemical, pharmaceutical, radioactive, electronic, animal, sharps, plastic and mixed waste.

## Slide 7
Summary of Major Regulatory Requirements
Essential EU Legislation for Biomedical Research Laboratories
Tier 1: Foundation & General Safety
REACH (EC No 1907/2006): Chemical registration, SDS compliance, and risk management.
Waste Framework Directive (2008/98/EC): Waste hierarchy and hazardous waste tracking.
OSH Framework Directive (89/391/EEC): Employer-led risk assessment and training.
Tier 2: Specialized Research & Ethical Compliance
Biological Agents (2000/54/EC): Containment for human tissue and cell culture.
GMO Legislation (2009/41/EC & 2001/18/EC): Protocols for viral vectors and CRISPR-organisms.
Animal Protection (2010/63/EU): The 3Rs principle and ethical oversight.
Tier 3: Environmental Protection
Water Framework Directive (2000/60/EC): Prohibition of chemical discharge.
Biocidal Products Regulation (EU 528/2012): Authorization for disinfectants.
Industrial Emissions (2010/75/EU): Compliance for large-scale operations.
Maintaining compliance across these three tiers is essential for legal operation, safety, and ethical research standards.

## Slide 8
International Sustainability Frameworks
Key certification and assessment programs for laboratory sustainability
My Green Lab
  The global leader in laboratory certification, focusing on energy, water, waste, and green chemistry for academic and industry sectors.
LEAF (Laboratory Efficiency Assessment Framework)
  Developed by UCL, this framework focuses on efficiency, equipment management, and procurement, widely adopted across European research institutions.
Global standard establishing an overall, top-down Environmental Management System (EMS).

## Slide 9
Measuring Quantifiable Key Performance Indicators (KPIs)
Leveraging frameworks like My Green Lab, LEAF, and ISO 14001 to drive lab sustainability
Energy Metrics
Monitor kWh/year, kWh/m², kWh/FTE, and publication- based intensity; prioritize freezer efficiency.
Waste & Plastics
Track total generation (kg/year), hazardous waste categories, recycling rates, and high-volume consumable usage.
Water & Utility
Audit consumption from inefficient autoclave and water purification systems.
Carbon Footprint
Measure Scope 1 (Direct), Scope 2 (Purchased electricity), and Scope 3 (Supply chain/travel) emissions.
Procurement & Storage
Assess sustainable product spend and optimize freezer occupancy/biobanking efficiency.
Data & Culture
Track server energy consumption, data storage TBs, staff training, and scientific reproducibility gains.

## Slide 10
Reducing Plastic Pollution
Examples of key strategies for mitigation
Better experimental planning
  Enhance research and operational protocols to reduce unnecessary material waste at the source.
Bulk purchasing
  Minimize packaging waste by procuring supplies in larger quantities to reduce single-use plastic consumption.
Recycling initiatives
  Improve waste management systems to ensure plastics are properly processed and diverted from landfills.
Shift to reusable alternatives
  Actively replace single-use plastic items with durable, long-term reusable solutions.

## Slide 11
~50%
of environmental footprint is tied directly to lack of scientific reproducibility

## Slide 12
Core Principles for Reproducible and Efficient Research
Power Calculations
Optimize sample sizes to achieve statistical power while minimizing resource consumption.
Randomization
Eliminate selection bias to ensure the integrity and reliability of experimental results.
Blinding
Implement rigorous masking protocols to prevent observer bias and maintain experimental objectivity.
Data Sharing
Promote transparency and scientific progress by making datasets accessible to the broader community.
Shared Controls
Leverage centralized control groups to reduce the total number of subjects required across multiple studies.
Robust Science is Inherently Green Science

## Slide 13
Focus on a single gene, protein, RNA, pathway, metabolite (or cell type).
Identify direct cause-and-effect relationships.
Highly controlled experiments.
Mechanistic depth.
From Reductionist to Systems Biology Approach

## Slide 14
Precision Medicine Paradigm
Balancing clinical impact vs. environmental cost
The high-throughput data
Electronic health records, imaging data, and multi-omics analysis.
Biobanking
Cardiovascular
Imaging
Clinical
Evaluation
Precision Medicine Environmental Dilemma
High-capacity computing
Artificial Intelligence modeling

## Slide 16
Cold Storage Optimization
Strategic Initiatives for Energy Efficiency and Space Management
Temperature adjustment
  Transition long-term storage from -80°C to -70°C to lower energy consumption.
Consolidation
  Optimize space by grouping samples and retiring underutilize freezer units.
Inventory purging
  Implement rigorous cycles to remove obsolete or expired samples.
Digital tracking
  Improve visibility through modernized inventory management systems.
A single standard -80°C ultra-low temperature freezer consumes as much energy as an entire average domestic household every single day (~20 kWh).
=
Inefficient freezer and sample management
Overfilled freezer
Storage of obsolete samples
Duplicate sample collections
Poor inventory tracking

## Slide 17
Sustainable Biobanking
Objective: Maximize biobank value while minimizing operational and environmental waste.
Centralized Storage
Consolidate assets to optimize energy usage and management efficiency.
Barcode Tracking
Implement standardized LIMS-based tracking for high-fidelity inventory management.
Apply FAIR principles
Ensure data is Findable, Accessible, Interoperable, and Reusable to prevent redundant data generation.
Shared Biobanks
Promote collaborative infrastructure to reduce redundancy and resource depletion.

## Slide 18
Global Environmental Change Advances 6 (2026)
Environmental AI Checklist
Ask whether AI is needed
Use the smallest effective model
Reuse existing models
Use efficient hardware and green data centers
Optimize inference and storage
Measure and report emissions

## Slide 19
Precision Medicine vs. Sustainability: Key Tensions
Balancing innovation with environmental responsibility
Precision Medicine Requirement
Sustainability Challenge
Large biobanks
Continuous freezer energy consumption
Multi-omics analyses
High plastic/reagent waste
AI & Bioinformatics
Intense computational energy demand
Sample/Data Retention
Storage footprint & resource intensity
Global Collaborations
Increased Scope 3 emissions
Precision medicine must maximize insight while minimizing environmental cost through optimized workflows, greener procurement, and clear environmental KPIs.

## Slide 20
The Solution: Sustainable Precision Medicine
Transitioning to a high-impact, low-footprint clinical research model
Smarter Biobanking
Optimizing storage temperatures and sample management to reduce energy consumption.
Greener Procurement
Prioritizing ACT-labelled products to ensure environmental accountability in the supply chain.
Efficient Omics Workflows
Streamlining high-throughput sequencing and analysis to minimize reagent waste and energy intensity.
Sustainable Cloud Computing
Leveraging energy-efficient data centers and optimized computing algorithms.
Data Retention Policies
Implementing lifecycle management to reduce the carbon footprint of unnecessary long-term cloud storage.
Dual KPI Framework
Tracking environmental sustainability metrics in parallel with traditional scientific performance indicators.

## Slide 21
The Future of Sustainable Cardiovascular Research
The environmental determinants of cardiovascular disease make sustainability in the research lab an integral part of our scientific mission.
Environmental safety and scientific excellence go hand in hand.
Sustainability must never compromise research quality.
The best cardiovascular laboratory is not defined solely by the impact of its discoveries, but also by its ability to generate those discoveries safely, ethically, reproducibly, and sustainably.
Reducing our research footprint is vital for both medical progress and planetary health.